## Slide 1: The Host
Xin Jin
Fall 2017 (TTh 1:30-2:45 in Malone 228）
EN.601.714 Advanced Computer Networks
https://github.com/xinjin/course-adv-net
Notes: Slides adapted from Princeton COS 561 Advanced Computer Networks

## Slide 2: Host-Network Division of Labor
Network
  Best-effort packet delivery
  Between two (or more) end-point addresses
Hosts
  Everything else
host
host
network

## Slide 3: The Role of the End Host
Network discovery and bootstrapping
  How does the host join the network?
  How does the host get an address?
Interface to networked applications
  What interface to higher-level applications?
  How does the host realize that abstraction?
Distributed resource sharing
  What roles does the host play in network resource allocation decisions?

## Slide 4: Network Discovery and Bootstrapping

## Slide 5: Relationship Between Layers
link
session
path
name
address

## Slide 6: Three Kinds of Identifiers
 | Host Name | IP Address | MAC Address
Example | www.cs.jhu.edu | 128.112.7.156 | 00-15-C5-49-04-A9
Size | Hierarchical, human readable, variable length | Hierarchical, machine readable, 32 bits (in IPv4) | Flat, machine readable, 48 bits
Read by | Humans, hosts | IP routers | Switches in LAN
Allocation, top-level | Domain, assigned by registrar (e.g., for .edu) | Variable-length prefixes, assigned by ICANN, RIR, or ISP | Fixed-sized blocks, assigned by IEEE to vendors (e.g., Dell)
Allocation, low-level | Host name, local administrator | Interface, by DHCP or an administrator | Interface, by vendor

## Slide 7: Learning a Host’s Address
Who am I?
  Hard-wired: MAC address
  Static configuration: IP interface configuration
  Dynamically learned: IP address configured by DHCP
Who are you?
  Hard-wired: IP address in a URL, or in the code
  Dynamically looked up: ARP or DNS
me
you
adapter
adapter

## Slide 8: Mapping Between Identifiers
Dynamic Host Configuration Protocol (DHCP)
  Given a MAC address, assign a unique IP address
  … and tell host other stuff about the Local Area Network
  To automate the boot-strapping process
Address Resolution Protocol (ARP)
  Given an IP address, provide the MAC address
  To enable communication within the Local Area Network
Domain Name System (DNS)
  Given a host name, provide the IP address
  Given an IP address, provide the host name

## Slide 9: Dynamic Host Configuration Protocol
arriving client
DHCP server
DHCP discover
(broadcast)
DHCP offer
DHCP request
DHCP ACK
(broadcast)
Host learns IP address,
Subnet mask, Gateway address, DNS server(s), and a lease time.

## Slide 10: Address Resolution Protocol (ARP)
Every host maintains an ARP table
  (IP address, MAC address) pair
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate and transmit the data packet
But, what if the IP address is not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches the result in its ARP table

## Slide 11: Domain Name System
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
Recursive query: #1
Iterative queries: #2, 4, 6

## Slide 12: DNS Root Servers
13 root servers (see http://www.root-servers.org/)
Labeled A through M
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software C. Palo Alto, CA (and 17 other locations)
I Autonomica, Stockholm (plus 3 other locations)
K RIPE London (also Amsterdam, Frankfurt)
m WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign, ( 11 locations)

## Slide 13: TLD and Authoritative DNS Servers
Top-level domain (TLD) servers
  Generic domains (e.g., com, org, edu)
  Country domains (e.g., uk, fr, ca, jp)
  Managed professionally (e.g., Educause for “edu”)
Authoritative DNS servers
  Provide public records for hosts at an organization
  For the organization’s servers (e.g., Web and mail)
  Can be maintained locally or by a service provider

## Slide 14: Questions
Should addresses correspond to the interface (point of attachment) or to the host?
Why do we have all three identifiers? Do we need all three?
What should be done to prevent spoofing of addresses?

## Slide 15: Interface to Applications

## Slide 16: Socket Abstraction
Best-effort packet delivery is a clumsy abstraction
  Applications typically want higher-level abstractions
  Messages, uncorrupted data, reliable in-order delivery
Applications communicate using “sockets”
  Stream socket: reliable stream of bytes (like a file)
  Message socket: unreliable message delivery
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 17: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 18: Two Main Transport Layers
User Datagram Protocol (UDP)
  Just provides demultiplexing and error detection
  Header fields: port numbers, checksum, and length
  Low overhead, good for query/response and multimedia
Transmission Control Protocol (TCP)
  Adds support for a “stream of bytes” abstraction
  Retransmitting lost or corrupted data
  Putting out-of-order data back in order
  Preventing overflow of the receiver buffer
  Adapting the sending rate to alleviate congestion
  Higher overhead, good for most stateful applications

## Slide 19: Questions
Is a socket between two IP addresses the right abstraction?
  Mobile hosts?
  Replicated services?
What does the network know about the traffic?
  Inferring the application from the port numbers?
Is end-to-end error detection and correction the right model?
  High loss environments?
  Expense of retransmitting over the entire path?

## Slide 20: Distributed Resource Sharing

## Slide 21: Resource Allocation Challenges
Best-effort network easily becomes overloaded
  No mechanism to “block” excess calls
  Instead excess packets are simply dropped
Examples
  Shared Ethernet medium: frame collisions
  Ethernet switches and IP routers: full packet buffers
Quickly leads to congestion collapse
Load
Goodput
“congestion
collapse”
Increase in load that results in a decrease in useful work done.

## Slide 22: End Hosts Adjusting to Congestion
End hosts adapt their sending rates
  In response to network conditions
Learning that the network is congested
  Shared Ethernet: carrier sense multiple access
    Seeing your own frame collide with others
  IP network: observing your end-to-end performance
    Packet delay or loss over the end-to-end path
Adapting to congestion
  Slowing down the sending rate, for the greater good
  But, host doesn’t know how bad things might be…

## Slide 23: Ethernet Back-off Mechanism
Carrier sense: wait for link to be idle
  If idle, start sending; if not, wait until idle
Collision detection: listen while transmitting
  If collision: abort transmission, and send jam signal
Exponential back-off: wait before retransmitting
  Wait random time, exponentially larger on each retry

## Slide 24: Transmission Control Protocol (TCP)
Stream-of-bytes service
  Sends and receives a stream of bytes
Reliable, in-order delivery
  Corruption: checksums
  Detect loss/reordering: sequence numbers
  Reliable delivery: acknowledgments and retransmissions
Connection oriented
  Explicit set-up and tear-down of TCP connection
Flow control
  Prevent overflow of the receiver’s buffer space
Congestion control
  Adapt to network congestion for the greater good

## Slide 25: Breaking a Stream of Bytes into TCP Segments

## Slide 26: TCP “Stream of Bytes” Service
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 80

## Slide 27: …Emulated Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out, or
“Pushed” by application.

## Slide 28: TCP Segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes on an Ethernet link
TCP packet
  IP packet with a TCP header and data inside
  TCP header is typically 20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 29: Sequence Number
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number = 1st byte
Byte 81

## Slide 30: Reliable Delivery on a Lossy Channel With Bit Errors

## Slide 31: Challenges of Reliable Data Transfer
Over a perfectly reliable channel
  Easy: sender sends, and receiver receives
Over a channel with bit errors
  Receiver detects errors and requests retransmission
Over a lossy channel with bit errors
  Some data are missing, and others corrupted
  Receiver cannot always detect loss
Over a channel that may reorder packets
  Receiver cannot distinguish loss from out-of-order

## Slide 32: TCP Support for Reliable Delivery
Detect bit errors: checksum
  Used to detect corrupted data at the receiver
  …leading the receiver to drop the packet
Detect missing data: sequence number
  Used to detect a gap in the stream of bytes
  ... and for putting the data back in order
Recover from lost data: retransmission
  Sender retransmits lost or corrupted data
  Two main ways to detect lost packets

## Slide 33: TCP Acknowledgments
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number = 1st byte
ACK sequence number = next expected byte

## Slide 34: Automatic Repeat reQuest (ARQ)
ACK and timeouts
  Receiver sends ACK when it receives packet
  Sender waits for ACK and times out
Simplest ARQ protocol
  Stop and wait
  Send a packet, stop and wait until ACK arrives
Time
Packet
ACK
Timeout
Sender
Receiver

## Slide 35: Flow Control: TCP Sliding Window

## Slide 36: Motivation for Sliding Window
Stop-and-wait is inefficient
  Only one TCP segment is “in flight” at a time
  Especially bad for high “delay-bandwidth product”
delay
bandwidth

## Slide 37: Numerical Example
1.5 Mbps link with 45 msec round-trip time (RTT)
  Delay-bandwidth product is 67.5 Kbits (or 8 KBytes)
Sender can send at most one packet per RTT
  Assuming a segment size of 1 KB (8 Kbits)
  8 Kbits/segment at 45 msec/segment  182 Kbps
  That’s just one-eighth of the 1.5 Mbps link capacity

## Slide 38: Sliding Window
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received

## Slide 39: Receiver Buffering
Receive window size
  Amount that can be sent without acknowledgment
  Receiver must be able to store this amount of data
Receiver tells the sender the window
  Tells the sender the amount of free space left
Window Size
Outstanding
Un-ack’d data
Data OK
to send
Data not OK
to send yet
Data ACK’d

## Slide 40: Optimizing Retransmissions

## Slide 41: Reasons for Retransmission
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS
Notes: Application may get duplicates in the case of early timeouts

## Slide 42: How Long Should Sender Wait?
Sender sets a timeout to wait for an ACK
  Too short: wasted retransmissions
  Too long: excessive delays when packet lost
TCP sets timeout as a function of the RTT
  Expect ACK to arrive after an “round-trip time”
  … plus a fudge factor to account for queuing
But, how does the sender know the RTT?
  Running average of delay to receive an ACK

## Slide 43: Example RTT Estimation

## Slide 44: Still, Timeouts are Inefficient

## Slide 45: Fast Retransmission
When packet n is lost…
  … packets n+1, n+2, and so on may get through
Exploit the ACKs of these packets
  ACK says receiver is still awaiting nth packet
  Duplicate ACKs suggest later packets arrived
  Sender uses “duplicate ACKs” as a hint
Fast retransmission
  Retransmit after “triple duplicate ACK”

## Slide 46: Effectiveness of Fast Retransmit
When does Fast Retransmit work best?
  High likelihood of many packets in flight
  Long data transfers, large window size, …
Implications for Web traffic
  Most Web transfers are short (e.g., 10 packets)
    So, often there aren’t many packets in flight
  Making fast retransmit is less likely to “kick in”
    Forcing users to click “reload” more often… 

## Slide 47: TCP Congestion Control

## Slide 48: TCP Congestion Control
Additive increase, multiplicative decrease
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
t
Window
halved
Loss
Other mechanisms: slow start, fast retransmit vs. timeout loss, etc.

## Slide 49: Congestion in a Drop-Tail FIFO Queue
Access to the bandwidth: first-in first-out queue
  Packets transmitted in the order they arrive
✗
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet

## Slide 50: How it Looks to the End Host
Delay: Packet experiences high delay
Loss: Packet gets dropped along path
How does TCP sender learn this?
  Delay: Round-trip time estimate
  Loss: Timeout and/or duplicate acknowledgments
✗

## Slide 51: TCP Congestion Window
Each TCP sender maintains a congestion window
  Max number of bytes to have in transit (not yet ACK’d)
Adapting the congestion window
  Decrease upon losing a packet: backing off
  Increase upon success: optimistically exploring
  Always struggling to find right transfer rate
Tradeoff
  Pro: avoids needing explicit network feedback
  Con: continually under- and over-shoots “right” rate

## Slide 52: Additive Increase, Multiplicative Decrease
How much to adapt?
  Additive increase: On success of last window of data, increase window by 1 Max Segment Size (MSS)
  Multiplicative decrease: On loss of packet, divide congestion window in half
Much quicker to slow than speed up!
  Over-sized windows (causing loss) are much worse than under-sized windows (causing lower thruput)
  AIMD: A necessary condition for stability of TCP

## Slide 53: Leads to the TCP “Sawtooth”
t
Window
halved
Loss

## Slide 54: Receiver Window vs. Congestion Window
Flow control
  Keep a fast sender from overwhelming a slow receiver
Congestion control
  Keep a set of senders from overloading the network
Different concepts, but similar mechanisms
  TCP flow control: receiver window
  TCP congestion control: congestion window
  Sender TCP window =
  min { congestion window, receiver window }

## Slide 55: Questions
What role should the network play in resource allocation?
  Explicit feedback to the end hosts?
  Enforcing an explicit rate allocation?
What is a good definition of fairness?
What about hosts who cheat to hog resources?
  How to detect cheating? How to prevent/punish?
What about wireless networks?
  Difficulty of detecting collisions
  Loss caused by interference, not just congestion

## Slide 56: A Protocol for Packet Network Intercommunication
(IEEE Trans. on Communications, May 1974)
Vint Cerf and Bob Kahn
Written when Vint Cerf was an assistant professor at Stanford, and Bob Kahn was working at ARPA.

## Slide 57: Life in the 1970s…
Multiple unconnected networks
  ARPAnet, data-over-cable, packet satellite (Aloha), packet radio, …
Heterogeneous designs
  Addressing, max packet size, handling of lost/corrupted data, fault detection, routing, …
ARPAnet
satellite net

## Slide 58: Handling Heterogeneity
Where to handle heterogeneity?
  Application process? End hosts? Packet switches?
Compatible process and host conventions
  Obviate the need to support all combinations
Retain the unique features of each network
  Avoid changing the local network components
Introduce the notion of a gateway

## Slide 59: Internetwork Layer and Gateways
Internetwork Layer
Gateway
Internetwork appears as a single, uniform entity
Despite the heterogeneity of the local networks
Network of networks
“Embed internetwork packets in local packet format or extract them”
Route (at internetwork level) to next gateway
ARPAnet
satellite net
gateway

## Slide 60: Internetwork Packet Format
Internetwork header in standard format
  Interpreted by the gateways and end hosts
Source and destination addresses
  Uniformly and uniquely identify every host
Ensure proper sequencing of the data
  Include a sequence number and byte count
Enable detection of corrupted text
  Checksum for an end-to-end check on the text
local
header
text
checksum
source
address
dest.
address
seq.
#
byte
count
flag
field
internetwork header

## Slide 61: Process-Level Communication
Enable pairs of processes to communicate
  Full duplex
  Unbounded but finite-length messages
  E.g., keystrokes or a file
Key ideas
  Port numbers to (de)multiplex packets
  Breaking messages into segments
  Sequence numbers and reassembly
  Retransmission and duplicate detection
  Window-based flow control

## Slide 62: Discussion
What did they get right?
  Which ideas were key to the Internet’s success?
  Which decisions still seem right today?
What did they miss?
  Which ideas had to be added later?
  Which decisions seem wrong in hindsight?
What would you do in a clean-slate design?
  If your goal wasn’t to support communication between disparate packet-switched networks
  Would you do anything differently?

## Slide 63: End-to-End Arguments in System Design
(ACM Trans. on Computer Systems, November 1984)
J. Saltzer, D. Reed, and D. Clark

## Slide 64: End-to-End Argument
Operations should occur only at the end points
… unless needed for performance optimization
2
4
5
3
1
Many things can go wrong: disk errors, software errors, hardware errors, communication errors, …

## Slide 65: Trade-Offs
Put functionality at each hop
  All applications pay the price
  End systems still need to check for errors
Place functionality only at the ends
  Slower error detection
  End-to-end retransmission wastes bandwidth
Compromise solution?
  Reliable end-to-end transport protocol (TCP)
  Plus file checksums to detect file-system errors

## Slide 66: Discussion
When should the network support a function anyway?
  E.g., link-layer retransmission in wireless networks?
Who’s interests are served by the e2e argument?
How does a network operator influence the network without violating the e2e argument?
Does the design of IP and TCP make it hard to violate the e2e argument?
  E.g., middlebox functionality like NATs, firewalls, proxies
Should the e2e argument apply to routing?

## Slide 67: Thanks! Q&A