## Slide 1: Control Plane
Xin Jin
Fall 2019 (TTh 1:30-2:45 in Hodson 316)
EN.601.714 Advanced Computer Networks
https://github.com/xinjin/course-adv-net
Notes: Slides adapted from Princeton COS 561 Advanced Computer Networks

## Slide 2: Data, Control, and Management Planes
 | Data | Control | Management
Time-scale | Packet (ns) | Event (10 ms to sec) | Human (min to hours)
Tasks | Forwarding, buffering, filtering, scheduling | Routing, signaling | Analysis, configuration
Location | Line-card hardware | Router software | Humans or scripts

## Slide 3: Routing vs. Forwarding
Routing: control plane
  Computing paths the packets will follow
  Routers talking amongst themselves
  Individual router creating a forwarding table
Forwarding: data plane
  Directing a data packet to an outgoing link
  Individual router using a forwarding table

## Slide 4: Data and Control Planes
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane

## Slide 5: Routing Protocols
What does the protocol compute?
  Spanning tree, shortest path, local policy, arbitrary end-to-end paths
What algorithm does the protocol run?
  Spanning-tree construction, distance vector, link-state routing, path-vector routing, source routing, end-to-end signaling
How do routers learn end-host locations?
  Learning/flooding, injecting into the routing protocol, dissemination using a different protocol, and directory server

## Slide 6: What Does the Protocol Compute?

## Slide 7: Different Ways to Represent Paths
Static model
  What is computed, i.e., what is the outcome
  Not how the (distributed) computation is performed
Trade-offs
  State required to represent the paths
  Efficiency of the resulting paths
  Ability to support multiple paths
  Complexity of computing the paths
  Which nodes are in charge
Applied in different settings
  LAN, intradomain, interdomain

## Slide 8: Spanning Tree
One tree that reaches every node
  Single path between each pair of nodes
  No loops, so can support broadcast easily
Disadvantages
  Paths are sometimes long
  Some links are not used at all

## Slide 9: Shortest Paths
Shortest path(s) between each pair of nodes
  Separate shortest-path tree rooted at each node
  Minimum hop count or minimum sum of edge weights
Disadvantages
  All nodes need to agree on the link metrics
  Multipath routing is limited to Equal Cost MultiPath

## Slide 10: Local Policy at Each Hop
Locally best path
  Local policy: each node picks the path it likes best
  … among the paths chosen by its neighbors
Disadvantages
  More complicated to configure and model
2
3
1
4
d
5
6
2
3
1
4
d
5
6
1 d
1 2 d
2 1 d
2 d
3 2 d
3 4 d
4 d
5 4 d
6 4 d
6 5 4 d
1 d
1 2 d
2 1 d
2 d
4 d
3 2 d
3 4 d
5 4 d
6 4 d
6 5 4 d

## Slide 11: End-to-End Path Selection
End-to-end path selection
  Each node picks its own end to end paths
  … independent of what other paths other nodes use
Disadvantages
  More state and complexity in the nodes
  Hop-by-hop destination-based forwarding is not enough

## Slide 12: How to Compute Paths?

## Slide 13: Spanning Tree Algorithm
Elect a root
  The switch with the smallest identifier
  And form a tree from there
Algorithm
  Repeatedly talk to neighbors
    “I think node Y is the root”
    “My distance from Y is d”
  Update info based on neighbors
    Smaller id as the root
    Smaller distance d+1
  Don’t use interfaces not in path
Used in Ethernet-based LANs
root
One hop
Three hops

## Slide 14: Spanning Tree Example: Switch #4
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
root
1
3
5
2
4
7
6

## Slide 15: Shortest-Path Problem
Compute: path costs to all nodes
  From a given source u to all other nodes
  Cost of the path through each outgoing link
  Next hop along the least-cost path to s
3
2
2
1
1
4
1
4
5
3
u
s
6

## Slide 16: Link State: Dijkstra’s Algorithm
S = {u}
for all nodes v
if (v is adjacent to u)
D(v) = c(u,v)
else D(v) = ∞
add w with smallest D(w) to S
update D(v) for all adjacent v:
D(v) = min{D(v), D(w) + c(w,v)}
until all nodes are in S
Flood the topology information to all nodes
Each node computes shortest paths to other nodes
Initialization
Loop
Used in OSPF and IS-IS

## Slide 17: Link-State Routing Example
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3

## Slide 18: Link-State Routing Example (cont.)
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3

## Slide 19: Link State: Shortest-Path Tree
Shortest-path tree from u
Forwarding table at u
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
v
(u,v)
w
(u,w)
x
(u,w)
y
(u,v)
z
(u,v)
link
s
(u,w)
t
(u,w)

## Slide 20: Distance Vector: Bellman-Ford Algorithm
Define distances at each node x
  dx(y) = cost of least-cost path from x to y
Update distances based on neighbors
  dx(y) = min {c(x,v) + dv(y)} over all neighbors v
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
du(z) = min{c(u,v) + dv(z),
c(u,w) + dw(z)}
Used in RIP and EIGRP

## Slide 21: Distance Vector: Count to Infinity
Link cost changes:
Good news travels fast
Bad news travels slow: “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 22: Path-Vector Routing
Extension of distance-vector routing
  Support flexible routing policies
  Avoid count-to-infinity problem
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
3
2
1
d
“d: path (2,1)”
“d: path (1)”
data traffic
data traffic
Used in BGP

## Slide 23: Path-Vector: Faster Loop Detection
Node can easily detect a loop
  Look for its own node identifier in the path
  E.g., node 1 sees itself in the path “3, 2, 1”
Node can simply discard paths with loops
  E.g., node 1 simply discards the advertisement
3
2
1
“d: path (2,1)”
“d: path (1)”
“d: path (3,2,1)”

## Slide 24: Path-Vector: Flexible Policies
Each node can apply local policies
  Path selection: Which path to use?
  Path export: Which paths to advertise?
Examples
  Node 2 may prefer the path “2, 3, 1” over “2, 1”
  Node 1 may not let node 3 hear the path “1, 2”
2
3
1
2
3
1

## Slide 25: End-to-End Signaling
Establish end-to-end path in advance
  Learn the topology (as in link-state routing)
  End host or router computes and signals a path
Routers support virtual circuits
  Signaling: install entry for each circuit at each hop
  Forwarding: look up the circuit id in the table
1
2
1: 7
2: 7
link 7
1: 14
2: 8
link 14
link 8
Used in MPLS with RSVP

## Slide 26: Source Routing
Similar to end-to-end signaling
  But the data packet carries the hops in the path
  … rather than the routers storing big tables
End-host control
  Tell the end host the topology
  Let the end host select the end-to-end path
Variations of source routing
  Strict: specify every hop
  Loose: specify intermediate points
Used in IP source routing (but almost always disabled)

## Slide 27: Questions
Compare link-state routing, distance-vector routing, path-vector routing, end-to-end signaling, and source routing
Notes: Link-state: disseminate topology information to all nodes, each node has the entire view and needs to run shortest path algorithms
Distance-vector: only know the distance to neighbors and neighbors’ path, do not have the global view
Only one entity computes and disseminate to all nodes?

## Slide 28: Learning Where the Hosts Are

## Slide 29: Finding the Hosts
Building a forwarding table
  Computing paths between network elements
  … and figuring out where the end-hosts are
  … to map a destination address to an outgoing link
How to find the hosts?
  Learning/flooding
  Injecting into routing protocol
  Dissemination via different protocol
  Directory service

## Slide 30: Learning and Flooding
When a frame arrives
  Inspect the source address
  Associate address with the incoming interface
When the frame has an unfamiliar destination
  Forward out all interfaces
  … except for the one where the frame arrived
A
B
C
D
Switch learns how to reach A.
A
B
C
D
When in doubt, shout!
Used in Ethernet LANs

## Slide 31: Inject into Routing Protocol
Treat the end host (or subnet) as a node
  And disseminate in the routing protocol
  E.g., flood information about where addresses attach
3
2
2
1
1
4
1
4
5
3
u
s
6
Used in OSPF and
IS-IS, especially in enterprise networks
. . .

## Slide 32: Disseminate With Another Protocol
Distribute using another protocol
  One router learns the route
  … and shares the information with other routers
learn a route to d
(e.g., via BGP)
disseminate route to other routers
Internal BGP (iBGP) used in backbone networks

## Slide 33: Directory Service
Contact a service to learn the location
  Lookup the end-host or subnet address
  … and learn the label to put on the packet
  … to get the traffic to the right egress point
s
d
i
e
directory
“Host d is at egress e”
Encapsulate packet to send to egress e.
Used in some data centers

## Slide 34: Conclusion
Routing is challenging
  Distributed computation
  Challenges with scalability and dynamics
Many different solutions for different environments
  Ethernet LAN: spanning tree, MAC learning, flooding
  Enterprise: link-state routing, injecting subnet addresses
  Backbone: link-state routing inside, path-vector routing with neighboring domains, and iBGP dissemination
  Data centers: many different solutions, still in flux
    E.g., link-state routing or multiple spanning trees
    E.g., directory service or injection of subnets into routing protocol

## Slide 35: Design Philosophy of the DARPA Internet Protocols (ACM SIGCOMM, 1988)
David Clark

## Slide 36: Design Goals
Primary goal
  Effective technique for multiplexed utilization of existing interconnected networks (e.g., ARPAnet, packet radio)
Important goals
  Survivability in the face of failure
  Multiple types of communication service
  Wide variety of network technologies
Less important goals
  Distributed management of resources
  Cost effectiveness
  Host attachment with low level of effort
  Accountability of resources

## Slide 37: Consequences of the Goals
Effective multiplexed utilization of existing networks
  Packet switching, not circuit switching
Continued communication despite network failures
  Routers don’t store state about ongoing transfers
  End hosts provide key communication services
Support for multiple types of communication service
  Multiple transport protocols (e.g., TCP and UDP)
Accommodation of a variety of different networks
  Simple, best-effort packet delivery service
  Packets may be lost, corrupted, or delivered out of order
Distributed management of network resources
  Multiple institutions managing the network
  Intradomain and interdomain routing protocols

## Slide 38: Questions
What if we started with different goals?
  Network management
  Less concern about backwards compatibility
  More concern about security
Can we address new challenges
  Management, security, privacy, sensor nets, …
  Without sacrificing the other goals?
  Without a major change to the architecture?

## Slide 39: End-to-End Routing Behavior in the Internet (ACM SIGCOMM, 1996; ToN, 1997)
Vern Paxson

## Slide 40: Measurement With Traceroute
Traceroute tool to measure the forwarding path
  Send packets with TTL=1, 2, 3…
  Record the source of the “time exceeded” message
Useful, but introduces many challenges
  Path changes
  Non-participating nodes
  Inaccurate, two-way measurements
source
destination
TTL=1
Time
exceeded
TTL=2

## Slide 41: Questions
Why can’t we measure the Internet more directly?
  What can we do about it?
Right division of labor between host and network?
  For path selection
  For network monitoring
How do we fix these routing problems, e.g., forwarding loops, path fluttering, and route asymmetry?
  In a decentralized, federated network
  How to incentivize better network management

## Slide 42: Backup Slides on Paxson Paper

## Slide 43: Paxson Study: Forwarding Loops
Forwarding loop
  Packet returns to same router multiple times
May cause traceroute to show a loop
  If loop lasted long enough
  So many packets traverse the loopy path
Traceroute may reveal false loops
  Path change that leads to a longer path
  Causing later probe packets to hit same nodes
Heuristic solution
  Require traceroute to return same path 3 times

## Slide 44: Paxson Study: Causes of Loops
Transient vs. persistent
  Transient: routing-protocol convergence
  Persistent: likely configuration problem
Challenges
  Appropriate time boundary between the two?
  What about flaky equipment going up and down?
  Determining the cause of persistent loops?
Anecdote on recent study of persistent loops
  Provider has static route for customer prefix
  Customer has default route to the provider

## Slide 45: Paxson Study: Path Fluttering
Rapid changes between paths
  Multiple paths between a pair of hosts
  Load balancing policies inside the network
Packet-based load balancing
  Round-robin or random
  Multiple paths for packets in a single flow
Flow-based load balancing
  Hash of some fields in the packet header
  E.g., IP addresses, port numbers, etc.
  To keep packets in a flow on one path

## Slide 46: Paxson Study: Routing Stability
Route prevalence
  Likelihood of observing a particular route
  Relatively easy to measure with sound sampling
  Poisson arrivals see time averages (PASTA)
  Most host pairs have a dominant route
Route persistence
  How long a route endures before a change
  Much harder to measure through active probes
  Look for cases of multiple observations
  Typical host pair has path persistence of a week

## Slide 47: Paxson Study: Route Asymmetry
Hot-potato routing
Other causes
  Asymmetric link weights in intradomain routing
  Cold-potato routing, where AS requests traffic enter at particular place
Consequences
  Lots of asymmetry
  One-way delay is not necessarily half of the round-trip time
Customer A
Customer B
multiple
peering
points
Provider A
Provider B
Early-exit
routing

## Slide 48: Thanks! Q&A