## Slide 1: EN.601.714 Advanced Computer Networks
Xin Jin
Fall 2017 (TTh 1:30-2:45 in Malone 228）
https://github.com/xinjin/course-adv-net
Notes: Slides adapted from Princeton COS 561 Advanced Computer Networks

## Slide 2: Introduction
Instructor: Xin Jin
  Malone 233, office hour Tuesday 2:45-4pm
  Research areas: computer networks, distributed systems
  Current projects: programmable networks, software-defined networking (SDN), big data analytics systems
  Cool projects available for project students, e.g., PhD qualifying projects
TA: Kaiyue (Karin) Wu
  Malone 207, office hour Tuesday 2:45-4pm

## Slide 3: The Internet: An Exciting Time
One of the most influential inventions
  A research experiment that escaped from the lab
  … to be a global communications infrastructure
Even wider reach
  Today: more than 3 billion users
  Tomorrow: more users, computers, things, ...
Near-constant innovation
  Apps: Web, P2P, social networks, virtual worlds
  Links: optics, WiFi, cellular, satellite, ...

## Slide 4: Transforming Everything
The ways we do business
  E-commerce, advertising, cloud computing, …
The way we communicate and socialize
  E-mail, Facebook, Instagram, WeChat, virtual worlds
How we think about law
  Interstate commerce? National boundaries?
The way we govern
  E-voting and e-government
  Censorship and wiretapping
The way we fight
  Cyber-attacks, including nation-state attacks

## Slide 5: But, What is Networking?

## Slide 6: A Plethora of Protocol Acronyms?
BGP
ARP
HTTP
DNS
PPP
OSPF
DHCP
TCP
UDP
SMTP
FTP
SSH
MAC
IP
RIP
NAT
CIDR
VLAN
VTP
NNTP
POP
IMAP
RED
ECN
SACK
SNMP
TFTP
TLS
WAP
SIP
IPX
STUN
RTP
RTSP
RTCP
PIM
IGMP
ICMP
MPLS
LDP
HIP
LISP
LLDP
BFD
Notes: Most have three or four letters, except IP has just two. But IP is special, as it is the center of the known universe.
Red: network layer
Green: transport layer
Purple: application layer
Blue: routing
Yellow: enterprise/edge networks
Black: other stuff
WAP: Wireless Application Protocol
SIP: Session Initiation Protocol
PPP: Point-to-Point Protocol
IPX: Internetwork Packet Exchange
HIP: Host Identity Protocol (HIP)
IGMP: Internet Group Management Protocol, multicast
ICMP: Internet Control Message Protocol, e.g., ping, traceroute
RTP: Real-time Transport Protocol
PIM: Protocol-Independent Multicast
RED: Random early detection
RTCP: RTP Control Protocol (RTCP)
RIP: Routing Information Protocol
SMTP: Simple Mail Transfer Protocol
RTSP: Real Time Streaming Protocol
BFD: Bidirectional Forwarding Detection
CIDR: Classless Inter-Domain Routing
NNTP: Network News Transfer Protocol
STUN: Session Traversal Utilities for NAT
VTP: VLAN Trunk Protocol
POP: Post Office Protocol
LISP: Locator/ID Separation Protocol
TFTP: Trivial File Transfer Protocol
LDP: Label Distribution Protocol

## Slide 7: A Heap of Header Formats?
Notes: Header formats have gotten more colorful in recent years, but they are still awfully boring. Zzzzz…
Have you seen the lego version of the IP and TCP header?

## Slide 8: TCP/IP Header Formats in Lego

## Slide 9: A Big Bunch of Boxes?
Router
Switch
Firewall
NAT
Load
balancer
DHCP
server
DNS
server
Bridge
Hub
Repeater
Base
station
Proxy
WAN
accelerator
Gateway
Intrusion
Detection
System
Packet
shaper
Route
Reflector
Label
Switched
Router
Scrubber
Packet
sniffer
Deep
Packet
Inspection
Notes: Ask yourself what is the real difference between these components? Do we need to think of them as distinct?
Can a common piece of hardware support many of these functions?
Do ever need to do more than one of these functions at the same time and place?

## Slide 10: A Ton of Tools?
traceroute
nslookup
ping
ipconfig
rancid
whois
tcpdump
wireshark
NDT
iperf
dummynet
syslog
trat
snort
bro
arpwatch
mrtg
nmap
ntop
dig
wget
net-snmp
Notes: nslookup: for dns
Nmap (Network Mapper): security scanner
Trat: TRaffic-Aware Topology control, reduce energy consumption
RANCID (The Really Awesome New Cisco config Differ): manage configurations
Ntop: network monitoring
dig: domain information groper
NDT: Network Diagnostic Tool
Mrtg:Multi Router Traffic Grapher is a tool to monitor the traffic load on network links

## Slide 11: A Ton of Tools?
traceroute
nslookup
ping
ipconfig
rancid
whois
tcpdump
wireshark
NDT
iperf
dummynet
syslog
trat
snort
bro
arpwatch
mrtg
nmap
ntop
dig
wget
net-snmp
Really Awesome New Cisco config Differ
Notes: nslookup: for dns
Nmap (Network Mapper): security scanner
Trat: TRaffic-Aware Topology control, reduce energy consumption
RANCID (The Really Awesome New Cisco config Differ): manage configurations
Ntop: network monitoring
dig: domain information groper
NDT: Network Diagnostic Tool
Mrtg:Multi Router Traffic Grapher is a tool to monitor the traffic load on network links

## Slide 12: What Do Peers in Other Fields Say?
“You networking people are very curious. You really love your artifacts.”
“In my college networking class I fell asleep at the start of the semester when the IP header was on the screen, and woke up at the end of the semester with the TCP header on the screen.”
“Network class final: ARP, DHCP, ICMP, IGMP, IP, TCP, UDP.”
Is networking “just the (arti)facts”?

## Slide 13: An Application Domain?
Notes: All of the next few slides have an element of truth in them. These are perfectly reasonable ways to think of networking as a “domain” rather than a “discipline”.

## Slide 14: Application Domain for Theory?
Algorithms and data structures
Control theory
Queuing theory
Optimization theory
Game theory and mechanism design
Formal methods
Information theory
Cryptography
Programming languages
Graph theory

## Slide 15: Application Domain for Systems?
Distributed systems
Operating systems
Computer architecture
Software engineering
…

## Slide 16: An Exercise in Entrepreneurship?
Identify a need or desirable capability
  Whether previously known or not
Invent a new feature or system that provides it
Determine how it fits in the existing network
Build and/or evaluate your solution
Pitch or $ell the problem and solution to others
  Whether to investors or a program committee
Bask in glory, or lick your wounds

## Slide 17: Now That I’ve Bummed You Out…
Or, Why Should You Stay in This Class,
and This Field?
Notes: These next few slides take the critiques in the previous slides and give them a positive spin. It’s not that the earlier slides were wrong, so much as there being an upside to all this…

## Slide 18: So, Why is Networking Cool?
Tangible, relates to reality
  Can measure/build things (we do “love our artifacts”)
  Can truly make far-reaching changes in the real world
Inherently interdisciplinary
  Well-motivated problems + rigorous solution techniques
  Interplay with policy, economics, and social sciences
Widely-read papers
  Many of the most cited papers in CS are in networking
  Congestion control, distributed hash tables, resource reservation, multimedia protocols, …
Notes: The point about widely-read papers is meant to be somewhat glib. High citation count doesn’t necessary mean important or deep – just that the field is large (and perhaps, as is true in networking, interdisciplinary). Or, maybe the networking field is just a large cult, where we all cite each others. ;)

## Slide 19: So, Why is Networking Cool?
Young, relatively immature field
  Great if you like to make order out of chaos
  Tremendous intellectual progress is still needed
  You can help decide what networking really is
Defining the problem is a big part of the challenge
  Recognizing a need, formulating a well-defined problem
  … is at least as important as solving the problem…
Lots of platforms for building your ideas
  Programmability: Click, OpenFlow/P4/NOX/Mininet, NetFPGA
  Routing software: Quagga, XORP, Bird, ExaBGP
  Testbeds: Emulab, PlanetLab, Orbit, GENI, …
  Measurements: RouteViews, traceroute, Internet2, …
Notes: The “lots of platforms” is relevant to the course, where we will leverage these platforms to Do Great Things.

## Slide 20: But, That Doesn’t Say What Networking Really Is
Or, What Will This Course Be About?

## Slide 21: One Take on Defining Networking
How to
  Design and operate components and protocols
  That may solve well-defined engineering problems
  That may can be used and combined in many ways
Definition and placement of function
  What to do, and where to do it
The “division of labor”
  Between the host, network, and management systems
  Across multiple concurrent protocols and mechanisms
  What makes a good division of labor?
Goal: search for general principles
  Of protocol and system design, evaluation, and composition

## Slide 22: What excites me about networking research
The introduction of new network functionality
The design of algorithms, protocols, and data structures that offer better performance, robustness, security, assurance, …
The art of system design for cleaner abstractions and easier management

## Slide 23: What Is This Course About?
The classics: Know from whence you came
  What problems were being solved?
  What were underlying assumptions that motivated the solutions?
… Applied to modern settings
  Datacenters as today’s warehouse computing
    New settings -> new problems and challenges
  Software-defined networking
    Remove legacy artifacts, provide more freedom to directly configure/program network

## Slide 24: Syllabus
Classics
Datacenter Networking
RDMA
Software-Defined Networking
Network Verification
Network Measurement
Middleboxes
Networking Meets Big Data

## Slide 25: Structure of the Course
Reading and analyzing research papers (20%)
  Design and evaluation of network protocols and systems
  Each student reviews 1 paper/class, submit reviews before the class
Classroom time: lectures and discussions (20%)
  Lectures on classics and background materials
  Discussion and debate about research papers
    Paper presentation (30min x 2): students give presentations with short QA; two papers each class, with optional readings
    Open discussion (15min): summaries, critiques, and comparisons of the papers
Programming assignments (20%)
  TCP performance and SDN
  Understanding network protocols empirically

## Slide 26: Structure of the Course
Final research project (40%)
  Novel research with a system-building component
    Open research problem: come up with your own, or talk to me
    Can work alone or in small teams, i.e., 1-5 people
    Must involve writing some software
  Can overlap with other projects, with permission
    Undergraduate research projects
    PhD qualifying research projects
  Deliverables
    Two-page short proposal: Oct 23
    Project presentation: Dec 7 (last class)
    Six-page final report: Dec 11
The goal is learning, not grades

## Slide 27: Getting Started…
Best-effort packet delivery service
Modularity through layering
Directories and routing
Data, control, and management planes

## Slide 28: Best-Effort Packet-Delivery Service
Notes: All of the next few slides have an element of truth in them. These are perfectly reasonable ways to think of networking as a “domain” rather than a “discipline”.

## Slide 29: Host-Network Division of Labor
Packet switching
  Divide messages into a sequence of packets
  Headers with source and destination address
Best-effort delivery
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
host
host
network

## Slide 30: Host-Network Interface: Why Packets?
Data traffic is bursty
  Logging in to remote machines
  Exchanging e-mail messages
Don’t want to waste bandwidth
  No traffic exchanged during idle periods
Better to allow multiplexing
  Different transfers share access to same links
Packets can be delivered by most anything
  RFC 1149: IP Datagrams over Avian Carriers

## Slide 31: Host-Network Interface: Why Best-Effort?
Never having to say you’re sorry…
  Don’t reserve bandwidth and memory
  Don’t do error detection & correction
  Don’t remember from one packet to next
Easier to survive failures
  Transient disruptions are okay during failover
Can run on nearly any link technology
  Greater interoperability and evolution

## Slide 32: Intermediate Transport Layer
But, applications want efficient, accurate transfer of data in order, in a timely fashion
  Let the end hosts handle all of that
  (An example of the “end-to-end argument”)
Transport layer can optionally…
  Detect and retransmit lost packets
  Put out-of-order packets back in order
  Detect and handle corrupted packets
  Avoid overloading the receiver
  <insert your requirement here>

## Slide 33: Modularity Through Layering
Notes: All of the next few slides have an element of truth in them. These are perfectly reasonable ways to think of networking as a “domain” rather than a “discipline”.

## Slide 34: IP Protocol Stack
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application

## Slide 35: IP Suite: End Hosts vs. Routers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 36: The “Narrow Waist” of IP
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Waist
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…
The waist facilitates interoperability
Notes: Abstract Internet Printing Protocol/NV (IPP/NV)
Trivial File Transfer Protocol (TFTP)

## Slide 37: Layer Encapsulation
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B

## Slide 38: Directories and Routing
Notes: All of the next few slides have an element of truth in them. These are perfectly reasonable ways to think of networking as a “domain” rather than a “discipline”.

## Slide 39: Relationship Between Layers
link
session
path
name
address

## Slide 40: Directories: Mapping Name to Address
link
session
path
name
address

## Slide 41: Types of Directories
Simplistic designs
  Ask everyone (e.g., flooding in ARP)
  Tell everyone (e.g., pushing /etc/hosts)
  Central directory
Scalable distributed designs
  Hierarchical namespace (e.g., DNS)
  Flat name space (e.g., Distributed Hash Table)

## Slide 42: Routing: Mapping Link to Path
link
session
path
name
address

## Slide 43: Path Computation
Spanning tree (e.g., Ethernet)
  One tree that connects every pair of nodes
Shortest paths (e.g., OSPF, IS-IS, RIP)
  Shortest-path tree rooted at each node
Locally optimal paths (e.g., BGP)
  Each node selects the best among its neighbors
End-to-end paths (e.g., source routing)
  Each node picks the best end-to-end path

## Slide 44: Data, Control, and Management Planes
Notes: All of the next few slides have an element of truth in them. These are perfectly reasonable ways to think of networking as a “domain” rather than a “discipline”.

## Slide 45: Inside the Network
Forward packets from the sender to the receiver

## Slide 46: Split into Data vs. Control Plane
Data plane: packets
  Handle individual packets as they arrive
  Forward, drop, or buffer
  Mark, shape, schedule, …
Control plane: events
  Track changes in network topology
  Compute paths through the network
  Reserve resources along a path
Motivated by need for high-speed packet forwarding

## Slide 47: Add the Management Plane
Making the network run well
  Traffic reaches the right destination
  Traffic flows over short, uncongested paths
  Unwanted traffic is discarded
  Failure recovery happens quickly
  Routers don’t run out of resources
A control loop with the network
  Measure (sense): topology, traffic, performance, …
  Control (actuate): configure control and data planes

## Slide 48: How to Read
You May Think You Already Know
How To READ, But…

## Slide 49: You Spend a Lot of Time Reading
Reading for grad classes
Reviewing conference submissions
Giving colleagues feedback
Keeping up with your field
Staying broadly educated
Transitioning into a new areas
Learning how to write better papers
It is worthwhile to learn to read effectively

## Slide 50: Keshav’s Three-Pass Approach: Step 1
A ten-minute scan to get the general idea
  Title, abstract, and introduction
  Section and subsection titles
  Conclusion and bibliography
What to learn: the five C’s
  Category: What type of paper is it?
  Context: What body of work does it relate to?
  Correctness: Do the assumptions seem valid?
  Contributions: What are the main research contributions?
  Clarity: Is the paper well-written?
Decide whether to read further…
Notes: Keep this in mind when you write your papers, so the readers (and reviewers) decide to read further…

## Slide 51: Keshav’s Three-Pass Approach: Step 2
A more careful, one-hour reading
  Read with greater care, but ignore details like proofs
  Figures, diagrams, and illustrations
  Mark relevant references for later reading
Grasp the content of the paper
  Be able to summarize the main idea
  Identify whether you can (or should) fully understand
Decide whether to
  Abandon reading in greater depth
  Read background material before proceeding further
  Persevere and continue for a third pass

## Slide 52: Keshav’s Three-Pass Approach: Step 3
Several-hour virtual re-implementation of the work
  Making the same assumptions, recreate the work
  Identify the paper’s innovations and its failings
  Identify and challenge every assumption
  Think how you would present the ideas yourself
  Jot down ideas for future work
When should you read this carefully?
  Reviewing for a conference or journal
  Giving colleagues feedback on a paper
  Understanding a paper closely related to your research
  Deeply understanding a classic paper in the field

## Slide 53: Other Tips for Reading Papers
Read at the right level for what you need
  “Work smarter, not harder”
Read at the right time of day
  When you are fresh, not sleepy
Read in the right place
  Where you are not distracted, and have enough time
Read actively
  With a purpose (what is your goal?)
  With a pen or computer to take notes
Read critically
  Think, question, challenge, critique, …

## Slide 54: How to write reviews
4 sections in review
  Summary
  Paper strengths
  Paper weaknesses
  Detailed comments
Summary (points in sentence or bullet form)
  1-2 points: What problem?
  1-2 points: Core novel ideas or technical contributions
  3-5 points: Summarize approach, mechanisms, findings

## Slide 55: How to write reviews
Strengths/Weaknesses: 2-4 points each
Detailed comments
  Longer exposition. Be constructive. Imagine conversation w/ authors: What would you tell them?
  May include
    Problem: What is it? Is it new? Is it real? Is it important?
    Solution: What is the technique(s)? Is it novel? How is it compared to past solutions? What is the intuition(s)?
    Implementation/evaluation: Does it have a real system prototype? Is the evaluation dataset(s) representative? Does the evaluation cover all aspects?
    Looking forward: Can you come up with a new/different/better solution? Can you find a new/related problem to solve?

## Slide 56: For Next Time
Sign up for paper presentations
  Each student sign up for two papers in different classes
  Instructions on course website
Read
  Original 1974 paper proposing TCP/IP
  The 1984 paper on the “end-to-end argument”
  (Submit reviews by next Monday)

## Slide 57: Thanks! Q&A